## Slide 1: IoT-Based Multi-Sensor Health Monitoring System
KNOWLEDGE INSTITUTE OF TECHNOLOGY

## Slide 2: OBJECTIVE, SOLUTION & IMPACT
Objective
Develop an IoT-based multi-sensor health monitoring system to continuously monitor heart rate, SpO₂, and body movement, while detecting abnormal movements such as falls.
Solution
Developed using ESP32, MAX30102, MPU6050, OLED display, and Wi-Fi to acquire, process, display, and remotely monitor health parameters in real time.
Impact
Provides a low-cost, compact, portable, and connected health monitoring solution for home healthcare, elderly monitoring, and remote patient observation.
KNOWLEDGE INSTITUTE OF TECHNOLOGY

## Slide 3: Engineering Design Process
Requirement & Planning:
Defined project objectives, identified health-monitoring requirements, selected physiological parameters, and designed the overall IoT-based system architecture.
System Development:
Developed heart-rate, SpO₂, movement, and fall-detection modules using MAX30102, MPU6050, and ESP32.
System Integration:
Integrated all sensing modules with the OLED display, Wi-Fi communication, and web-based monitoring interface into a unified health monitoring system.
Testing & Validation:
Evaluated sensor readings, fall detection, OLED display, Wi-Fi communication, and real-time monitoring under laboratory conditions.
KNOWLEDGE INSTITUTE OF TECHNOLOGY

## Slide 4: Process Table
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Phase | Engineering Steps | Key Activities & Outcome
I. Definition | Requirement Analysis, Concept Design | Defined: Need for continuous health monitoring and remote observation. Concept: IoT-based multi-sensor health monitoring system using ESP32, MAX30102, and MPU6050.
II. Development | System Design, Module Development, Integration | Developed: Heart-rate, SpO₂, and fall-detection modules. Integrated: OLED display, Wi-Fi communication, and web-based monitoring.
III. Realization | Prototype, Testing, Validation | Built: Functional health monitoring prototype. Validated: Sensor operation, real-time monitoring, fall detection, and wireless communication.

## Slide 5: List of Activities
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Literature Survey:
Studied IoT-based healthcare, wearable health monitoring, physiological sensors, and fall-detection techniques.
B. Requirement Analysis:
Identified system requirements, health parameters, components, and overall architecture.
C. Sensor & Controller Selection:
Selected ESP32, MAX30102, MPU6050, and OLED display according to system requirements.
D. Hardware Development:
Integrated the ESP32 controller, sensors, OLED display, power supply, and electrical connections.
E. Software Development:
Developed the embedded program for sensor acquisition, processing, display, and Wi-Fi communication.
F. System Integration:
Combined physiological monitoring, fall detection, OLED display, and remote monitoring into a single system.
G. Testing & Validation:
Tested sensor readings, fall detection, Wi-Fi communication, display operation, and overall system performance.

## Slide 6: Activity Duration Table
ID | Activity Description | Duration (Hours)
A | Requirement Engineering | 30
B | Concept Design | 27
C | Embodiment & Detail Design | 42
D | Software Development | 55
E | System Integration | 28
F | Testing & Optimization | 38
G | Documentation & Presentation | 30
Total | Project Duration | 250 Hours
KNOWLEDGE INSTITUTE OF TECHNOLOGY

## Slide 7: Activity Precedence Table
ID | Activity | Predecessor
A | Requirement Engineering | —
B | Concept Design | A
C | Embodiment Design | B
D | Detail Design | C
E | Software Development | D
F | System Integration | E
G | Testing & Optimization | F
H | Documentation & Presentation | G
KNOWLEDGE INSTITUTE OF TECHNOLOGY

## Slide 8: Glossary:
KNOWLEDGE INSTITUTE OF TECHNOLOGY
IoT (Internet of Things):
Technology that enables connected devices to collect, process, and exchange health data.
ESP32:
Microcontroller with integrated Wi-Fi used as the central processing and communication unit.
MAX30102:
Optical sensor used for heart-rate and SpO₂ measurement.
MPU6050:
Inertial sensor containing an accelerometer and gyroscope for movement and fall detection.
PPG (Photoplethysmography):
Optical technique used to detect blood-volume changes for physiological monitoring.
SpO₂:
Peripheral oxygen saturation, representing the percentage of oxygen-saturated blood.
BPM:
Beats Per Minute, the unit used to represent heart rate.
I²C:
Inter-Integrated Circuit communication protocol used for sensor and display interfacing.

## Slide 9: Core Technologies & Principles
KNOWLEDGE INSTITUTE OF TECHNOLOGY
IoT:
Enables wireless transmission of health information for remote monitoring.
Photoplethysmography (PPG):
Uses optical sensing to measure blood-volume variations for heart-rate and SpO₂ monitoring.
Embedded Processing:
ESP32 acquires, processes, and manages sensor information.
Motion Sensing:
MPU6050 measures acceleration and orientation changes for movement and fall detection.
I²C Communication:
Provides communication between ESP32, MAX30102, MPU6050, and OLED display.
Wi-Fi Communication:
Enables wireless transmission of real-time health information to the monitoring interface.
Real-Time Monitoring:
Continuously displays and updates health parameters and fall status..

## Slide 10: Concept Rules & Laws
KNOWLEDGE INSTITUTE OF TECHNOLOGY
PPG Principle:
Changes in blood volume produce variations in detected light, which are used to determine physiological parameters.
Heart Rate Measurement:
Periodic variations in the PPG signal are processed to calculate heart rate in BPM.
SpO₂ Measurement:
Red and infrared optical signals are used to estimate blood oxygen saturation.
Motion Detection Principle:
Changes in acceleration and orientation are analysed to identify abnormal movements and possible falls.
Embedded System Principle:
ESP32 continuously acquires and processes sensor data to generate monitoring outputs.
Real-Time Monitoring:
Health parameters are continuously processed and displayed locally and remotely.

## Slide 11: System Components & Technologies
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Technology | Purpose
ESP32 | Main controller and Wi-Fi communication
MAX30102 | Heart-rate and SpO₂ measurement
MPU6050 | Movement and fall detection
OLED Display | Real-time health-parameter display
Arduino IDE | Embedded software development
I²C | Sensor and display communication
Wi-Fi | Wireless data transmission
Web Server | Remote health monitoring
USB Power Supply | Provides power to the prototype

## Slide 12
KNOWLEDGE INSTITUTE OF TECHNOLOGY
System Model
Human / Patient
Heart Rate + SpO₂ + Body Movement
MAX30102 + MPU6050
ESP32
OLED Display
Wi-Fi
Web-Based Monitoring Interface
Heart Rate + SpO₂ + Fall Detection Statu

## Slide 13: What-if-Analysis
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Scenario | Expected System Response
Normal Health Condition | Displays current heart-rate and SpO₂ values on the OLED and monitoring interface.
Abnormal Movement Detected | MPU6050 identifies sudden acceleration or orientation changes.
Fall Detected | Displays fall status and updates the monitoring interface.
Wi-Fi Connected | Transmits health information for remote monitoring
Wi-Fi Unavailable | Local OLED monitoring remains available, but remote monitoring is affected.
Excessive Movement | MAX30102 readings may become unstable because of motion artifacts.

## Slide 14: Conclusion
KNOWLEDGE INSTITUTE OF TECHNOLOGY
The IoT-Based Multi-Sensor Health Monitoring System successfully monitors heart rate, SpO₂, body movement, and fall detection in real time.
The system uses ESP32, MAX30102, MPU6050, OLED display, and Wi-Fi to acquire, process, display, and transmit health information.
The prototype successfully demonstrates continuous health monitoring, fall detection, local visualization, and wireless remote monitoring.
The project demonstrates the practical application of IoT, embedded systems, and biomedical sensing technologies in healthcare and provides a foundation for future wearable and intelligent health-monitoring applications.
.